## Slide 1: Missing Middle Housing
Association of Bay Area Governments Month xx, 2021
Presenter: xxxxxxxxxxx

## Slide 2: Shifting demand for walkable living and MMH
Chart: Millennials (25-34)
| Single Family | Mobile Homes | Multifamily | Condos | Townhomes
Millennials (25-34) | 39 | 2 | 15 | 10 | 34
Chart: Baby Boomers (55-64)
| Single Family | Mobile Homes | Multifamily | Condos | Townhomes
Baby Boomers (55-64) | 71 | 2 | 7 | 9 | 11
  Diagram source: realtor.com

## Slide 3: What Missing Middle Housing is
House-scale buildings with multiple units in walkable neighborhoods

## Slide 4: House-Scale with multiple units
Width, Depth: Footprint of small to large houses
“House-Scale”
© 2017 Opticos Design, Inc. |
  Photo source: Opticos Design Inc
Notes:   Need to get beyond subsidized affordable housing as the only tool for affordable housing

## Slide 5: In Walkable Neighborhoods: What Can I Walk To?
Missing Middle Ready Contexts:
Ideally, the parcels within short walking distance of services, food, shopping, or transit
Alternatively, areas within short walking distance of other amenities: parks and schools
1
2

## Slide 6: The Palette of Missing Middle Housing Types
+

## Slide 7: Duplex: Side-by-Side
Typical Lot Size | Density
55’ x 100’ | 16 du/acre
55’ x 150’ | 10.6 du/acre
50’ x 100’ | 17.4 du/acre
Resultant Density: 11 to 17 per acre
  Photo source: Google Street Views

## Slide 8: Duplex: Stacked
Typical Lot Size | Density
50’ x 130’ | 13 du/acre
50’ x 100’ | 17.4 du/acre
35’ x 100’ (w/alley) | 25 du/acre
Resultant Density: 13 to 25 per acre

## Slide 9: Cottage Court (Bungalow Court)
Typical Lot Size | Density
110 x 205 (10 cottages) | 19 du/acre
110 x 205 (8 cottages) | 15 du/acre
Resultant Density: 15 to 19 per acre
  Photo source: Google Street Views

## Slide 10: Triplex / Fourplex
Typical Lot Size | Density
50’ x 140’ (4 units) | 25 du/acre
50’ x 120’ (4 units) | 29 du/acre
60’ x 120’ (4 units) | 24 du/acre
Resultant Density: 24 to 29 per acre

## Slide 11: Multiplex Small (Mansion)
Typical Lot Size | Density
85’ x 115’ (5 units) | 22 du/acre
85’ x 115’ (6 units) | 27 du/acre
Resultant Density: 22 to 27 per acre

## Slide 12: Multiplex Large (Mansion)
Typical Lot Size | Density
95’ x 115’ (12 units w/alley) | 48 du/acre
105’ x 135’ (12 units) | 37 du/acre
Resultant Density: 37 to 48 per acre

## Slide 13: Courtyard (Neighborhood Courtyard)
Typical Lot Size | Density
125’ x 150’ (8 units) | 18du/acre
125’ x 150’ (12 units) | 28 du/acre
100’ x 110’ (8 units) | 31.7 du/acre
Resultant Density: 18 to 32 per acre

## Slide 14: Townhouse: Small
Typical Lot Size | Density
80’ x 100’ (3 townhouses) | 16 du/acre
100’ x 100’ (4 townhouses) | 17.5 du/acre
Resultant Density: 16 to 18 per acre
  Photo source: Google Street Views

## Slide 15: Townhouse: Large
Typical Lot Size | Density
25’ x 125’ (1 townhouse) | 14 du/acre
25’ x 105’ (1 townhouse) | 17 du/acre
120’ x 105’ (8 townhouses) | 29 du/acre
Resultant Density: 14 to 29 per acre

## Slide 16: Using attic stories to increase housing
An attic story is entirely within the volume of the roof and adds habitable space to the building without adding another story
2 stories with a 3rd story within the roof volume/attic space
3 stories
2 stories with a 3rd story within the roof volume/attic space

## Slide 17: Strategies
1) Distributed Throughout a Block with Single-Family Homes
2) On the End-Grain of a Single-Family Block
3) Transition from Single-Family to Higher-Intensity Housing
4) Transition from Single-Family to a Mixed-Use Corridor

## Slide 18: MMH Example: Bungalows on the lake at Prairie Queen 50 acres – 742 Dwelling Units, Density (gross): 14.8 du/ac Building Types: Duplex, Fourplex, Multiplex Small & Large, Townhouse Location: Papillion, Nebraska
© 2016 Opticos Design, Inc. |
  Photo source: Urban Waters

## Slide 19: MMH Example: Daybreak Mews Home 3.2 acres – 65 Dwelling Units, Density (gross): 20 du/ac Building Types: Mews (Townhouse located along a Mews) Location: South Jordan, Utah
© 2016 Opticos Design, Inc. |
Notes: Mews: Buildings with their entries and living areas along a linear pedestrian-only shared space that links two or more ends of a block. `

## Slide 20: MMH Example: Dekum/Charles Converted Fourplex 0.11 acres – 4 Dwelling Units, Density (net): 35 du/ac Building Types: Fourplex Location: Portland, Oregon
© 2016 Opticos Design, Inc. |
Before
After
  Photo source: Garlynn Woodsong

## Slide 21: MMH Example: Riverhouse Pocket Neighborhood 1.37 acres – 12 Dwelling Units, Density (gross): 8.7 du/ac Building Types: Small Houses Location: Healdsburg, California
© 2016 Opticos Design, Inc. |
  Site plan photo source: riverhousehealdsburg.com
Notes: Pocket Neighborhood: A group of 5 to 10 detached, House-Scale Buildings each containing one to four units, arranged to define a shared open space.

## Slide 22: Barrier: Maximum Residential Density Nearly the same density but totally different
Density = 30 units per acre
Density = 29 units per acre
49 units in this building
5 units in this building
  Photo source: Google Street View

## Slide 23: MMH Barrier: Maximum Residential Density Why Does This Matter?
Missing Middle Housing exceeds most community’s max density limits. ​
The majority of existing density maximums are based on large developments and not infill lots.
Per acre
Per acre
Per acre
8
5
14

## Slide 24: MMH Barrier: Infill Lots are typically not served well by Multifamily Zoning
Max. Density allows 18 units per acre Result: 0 units Reason: side buffer requirement for multifamily
Missing Middle Option Result: 5 units (18/acre), 8 units (29/acre) Reason: House-scale building with similar building footprint and same setbacks as rest of neighborhood
Remove buffer requirements Use same setbacks as for houses Remove on-site open space requirements Treat vehicle access same as for houses

## Slide 25: Barrier: Minimum unit size requirements
Allow more units below 1,000 SF
Mix of Unit Sizes
Smaller Units Need More Design Consideration
  How Many 1,000 SF or Smaller Units Are on Market Right Now?
  Photo source: Urban Waters

## Slide 26: Barrier: Parking Often, not coordinated with lot size(s)
Parking fits on same lot as building
Neighboring lot added to meet parking requirement
  Photo source: Google Street View

## Slide 27: Implementation
New Standards Set of additional content and standards inserted as overlay standards; can include some changes to existing standards
Replacement of Zone(s) New zone district(s) and standards to replace the zone(s) that apply to one or several neighborhoods
Code Update Zone(s) and standards that replace existing zone(s) and standards plus other related improvements
Lower Effort / Lower Cost
Higher Effort / Higher Cost
Targeted Changes to Existing Zoning Standards
Edit existing standards zone-wide or only for specific areas

## Slide 28: Questions? Resources: Association of Bay Area Governments